## Slide 1: Group D: RTI Settings Experiment Georgia O’Keeffe Museum
Members:
Anthony Casaretto
Aaron Jauregui
April Mao
Kevin Neal

## Slide 2
What is RTI?:
The RTI is a software interface to a set of tools that process your captured image set to produce RTI files.
purple arrows : normals of the picture

## Slide 3: Normal Mapping
A technique used for faking lighting of 3D to 2D image
Normal maps are stored as regular RGB images
Notes: Add normal map from final set here

## Slide 4: What is ISO?
Film Speed
Higher ISO = More noise/ More sensitive to light

## Slide 5: Equipment
Canon EOS 650D DSLR
Light Dome
Test Object

## Slide 6
Take pictures:
ISO 100-12800
Generate normal maps with RTI Viewer
Make Matlab program to compare normal maps
error between the base ISO average (100) and the averages of the other ISOs
Run Matlab program on normal map pictures
Procedure
ISOTEST.m

## Slide 7: Problems and Solutions
Problem: Compared pixel’s RGB values
  Calculate standard deviation
Solution: Compare EACH pixel’s RGB vector angle
  Calculate the mean

## Slide 8: Low Resolution Results

## Slide 9: Low Resolution Results

## Slide 10: High Resolution Results

## Slide 11: High Resolution Results

## Slide 12: Algorithm Test (Rotate Image)

## Slide 13: Conclusion
Higher ISO = Higher error = More noise
More significant at higher resolution
Lower resolution = minimal difference
Higher resolution = relevant difference

## Slide 14: To the future user...
New tests to run:
  Light distance
  Dome distance
Rerun ISO experiment:
  Larger domes
  Larger/different test objects
Matlab Code - Needs to be optimized

## Slide 15
Questions?

## Slide 16: Acknowledgements
Thanks to Jing Liu for providing scripts to create the RTI files.
Thanks to Bipeng Zhang for help debugging with MatLab.
Thanks to Cultural Heritage Imaging for the RTI viewer software.
Thanks to Breeze Systems for the open source tool DSLR remote pro.
Thanks to James Davis for being helpful in guiding us during the process of this project.

## Slide 17: Tasks
Familiarized ourselves with use of the dome
Took some sample data using different ISO settings; created 2 RTI files for 5 different ISOs. Made note that as we increased ISO, the images not only got brighter, but the normal maps became more grainy.
Got a better test object: small, square, oil painting that should fit inside the dome much better.
Got a decent workflow going using the USB cable; data collection still relatively slow, but good enough for this experiment.
Obtained ISO data set for analysis: tested 8 ISOs, 100, 200, 400, 800, 1600, 3200, 6400, and 12800. Make 5 RTI-viewer files for each ISO.
Worked with FreeMat: Wrote program that compares the normal values for each pixel of the normal maps.
Analyzed and improved the MatLab code to provide more useful plots. Got consistency test working properly.
Obtained a new data set using a longer shutter speed to make for more balance of dark to light ratio in images. Made sure setup would allow us to easily crop the final normal map files.
Started working with MatLab to analyze the data.
Cropped the images from final ISO data set.
Obtained our 2 plots